ANGLE 1

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain "ANGLE 1" made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon), which can be removed, water sealing height of 34mm, with hoop and flange for hydro isolation, which also can be removed if necessary, height-adjustable carrier of a grid and hair stopper.

Stainless steel grid "ANGLE" class K3 (up to 300 kg of load) dimensions of 194x194 mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

ANGLE 2

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain "ANGLE 2" made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 71mm and flow rate of 0.80 l/s.

Base of drain without socket (siphon), water sealing height of 28mm, with hoop and flange for hydro isolation, which can be removed if necessary, height-adjustable carrier of a grid and hair stopper.

Stainless steel grid "ANGLE" class K3 (up to 300 kg of load) dimensions of 144x144 mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

ANGLE VERTICAL

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain "VERTICAL ANGLE" made of PP with no side inlets, with one vertical DN 50mm outlet, minimum installation height of 69mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a vertical drain, which can be removed, water sealing height of 30mm, with hoop and flange for hydro isolation, which also can be removed if necessary, height-adjustable carrier of a grid and hair stopper.

Stainless steel grid "ANGLE" class K3 (up to 300 kg of load) dimensions of 194x194 mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

ANGLE 1 GOLD

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain "ANGLE 1 GOLD" made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon), which can be removed, water sealing height of 34mm, with hoop and flange for hydro isolation, which also can be removed if necessary, height-adjustable carrier of a grid and hair stopper.

24k gold plated stainless steel mask for grid carrier and 24k gold plated stainless steel grid "ANGLE" class K3 (up to 300 kg of load) dimensions of 194x194 mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.