STANDARD CERAMIC DRY 1

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain "STANDARD CERAMIC DRY 1" made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask and ceramic holder dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

STANDARD CERAMIC DRY 2

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " STANDARD CERAMIC DRY 2" made of PP with one horizontal side inlet DN40 and with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask and tempered black glass dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

STANDARD CERAMIC DRY 3

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " STANDARD CERAMIC DRY 3" made of PP with three horizontal side inlets DN40 and with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask and ceramic holder dimensions of 94x94mm.Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

STANDARD CERAMIC DRY 4

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " STANDARD CERAMIC DRY 4" made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 71mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask and ceramic holder dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

STANDARD CERAMIC VERTICAL DRY

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain "VERTICAL STANDARD CERAMIC DRY  " made of PP with no side inlets, with one vertical DN 50mm outlet, minimum installation height of 69mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 30mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask and ceramic holder dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

STANDARD CERAMIC DRY GOLD

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " STANDARD CERAMIC DRY GOLD" made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

24k gold plated stainless steel mask for grid carrier and ceramic holder dimiesions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.