BLACK GLASS DRY 1

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain "BLACK GLASS DRY 1 " made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask for grid carrier and tempered black glass dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

BLACK GLASS DRY 2

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " BLACK GLASS DRY 2 " made of PP with one horizontal side inlet DN40 and with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask for grid carrier and tempered black glass dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

BLACK GLASS DRY 3

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " BLACK GLASS DRY 3 " made of PP with three horizontal side inlets DN40 and with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask for grid carrier and tempered black glass dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

BLACK GLASS DRY VERTICAL

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " BLACK GLASS VERTICAL DRY " made of PP with no side inlets, with one vertical DN 50mm outlet, minimum installation height of 69mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 30mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask for grid carrier and tempered black glass dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

BLACK GLASS  GOLD

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " BLACK GLASS GOLD" made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

24k gold plated stainless steel mask and  tempered black glass dimiesions of 94x94 mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

WHITE GLASS DRY 1

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " WHITE GLASS DRY 1 " made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask for grid carrier and tempered white glass dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

WHITE GLASS DRY 2

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " WHITE GLASS DRY 2 " made of PP with one horizontal side inlet DN40 and with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask for grid carrier and tempered white glass dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.

WHITE GLASS DRY 3

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " WHITE GLASS DRY 3 " made of PP with three horizontal side inlets DN40 and with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask for grid carrier and tempered white glass dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions

WHITE GLASS DRY VERTICAL

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " WHITE GLASS VERTICAL DRY " made of PP with no side inlets, with one vertical DN 50mm outlet, minimum installation height of 69mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 30mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

Stainless steel mask for grid carrier and tempered white glass dimensions of 94x94mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions

WHITE GLASS  GOLD

Procurement, transport and installation of floor grates and drains CONFLUO STANDARD intended for point drainage inside the building.

CONFLUO STANDARD drain " WHITE GLASS GOLD" made of PP with no side inlets, with one horizontal DN 50mm outlet adjustable under the angle of 15° maximum, minimum installation height of 64mm and flow rate of 0.80 l/s.

Base of drain with a socket (siphon) of a dry drain, which can be removed, water sealing height of 38mm, with hoop for hydro isolation which also can be removed if necessary and in which it is possible to attach flange for hydro isolation and height-adjustable carrier of a grid.

24k gold plated stainless steel mask and tempered white glass dimiesions of 94x94 mm.

Floor grates and drains should be "PEŠTAN" Aranđelovac type or equivalent quality. Installation of drains is done by achieving watertight connection with waterproofing layer of the floor, all in accordance with the relevant European and national standards, and according to the manufacturer's instructions.